## Slide 1
UC8: ROBOTIC ARM CONVEYOR PICK-AND-PLACE
WITH OBSTACLE AVOIDANCE
Milestone 1 Official Defense & Technical Evaluation (Week 05)
PROJECT METADATA
• Course: Robotic Project — Vietnamese-German University
• System: UR10e (6-DOF) + 3.6m Conveyor + 2-Finger Claw + 3 Bins
• Evaluation: Milestone 1 Official Defense (Requirements R1 - R4)
• Next Phase: Week 06 Sprint & Milestone 2 (Static Obstacle Avoidance)
• Empirical Status: 100% Verified Closed-Loop Sequencer (70/70 Trials OK)
MILESTONE 1 VERIFIED HIGHLIGHTS
✔ UR10e Motion Streaming: 50 Hz /joint_states driving 6 ArticulationBodies
✔ Industrial 2-Finger Claw: Procedural flange mount, status LED, aluminum arms
✔ Autonomous Sequencer: 7-step closed-loop state machine (zero human input)
✔ Zero-Teleport Physics: Pure friction coasting stop halting cubes (±3mm precision)
✔ Quality Assurance: 70 consecutive trials logged with 100% success rate

## Slide 2
PRESENTATION STRUCTURE
Agenda of Milestone 1 Defense & Roadmap
UC8 Robotic Sorting Workcell | Milestone 1 Defense | Vietnamese-German University
Slide 02
No. | Topic | Core Content & Engineering Focus
01-02 | Project Title & Agenda | Context, requirements, and presentation structure
03-04 | Baseline Recap & Scope Fulfillment | 100% completion of Milestone 1 commitments (R1-R4)
05 | System Architecture | Bidirectional closed loop: Unity 2022.3 <-> ROS-TCP <-> ROS Noetic
06 | Feedback & Issue Resolutions | Faculty claw feedback, anti-miss scanner, orthogonal zero-sink grasp
07-08 | Workcell Layout & Kinematics | Option 1 bilateral symmetry, 90° wrist lock, pure base SCARA sweep
09-10 | PhysX Simulation & State Machine | Friction deceleration, multi-item flow, 7-step sequencer
11-12 | Benchmark QA & Technical Defenses | 70 empirical trials, 100% success rate, answers to faculty committee
13-14 | Week 06 Objectives & Milestone 2 Roadmap | R5 conveyor robustness, vision classification, static obstacle avoidance
15 | Summary & M1 Acceptance Conclusion | Milestone 1 criteria sign-off and transition to Milestone 2 development

## Slide 3
BASELINE VS COMMITMENTS
Week 04 Baseline and Commitments Set Out for Milestone 1
UC8 Robotic Sorting Workcell | Milestone 1 Defense | Vietnamese-German University
Slide 03
Baseline Achieved in Week 04
✔ ROS-Unity bridge: TCP communication established on port 10000 via ros_tcp_endpoint.
✔ Coordinate conversion: Unity coordinates mapped to ROS FLU: X_ROS = Z_Unity, Y_ROS = -X_Unity, Z_ROS = Y_Unity.
✔ Object perception: /detected_object_pose (Pose) and /detected_object_type (String) published at 10 Hz.
✔ MoveIt planning: Pre-grasp feasibility verified in RViz (+15cm hover pose above detected cube base).
Commitments Set Out for Milestone 1
🎯 Trajectory execution: Overcome 'plan-only' barrier; stream real-time joint-states to drive physical UR10e in Unity.
🎯 Grasping mechanism: Implement attach/parenting logic linking target cube to tool0 upon arrival.
🎯 Task controller: Construct autonomous closed-loop sequencer connecting perception, motion, and release.
🎯 Multi-bin sorting: Route red, yellow, and blue cubes to dedicated destination bins without collision.
🎯 Milestone 1 Context: Fulfilling 100% of these commitments in Week 04 is the prerequisite for Milestone 1.

## Slide 4
EXECUTION AND SCOPE
Milestone 1 Scope: 100% Commitment Fulfillment Status
UC8 Robotic Sorting Workcell | Milestone 1 Defense | Vietnamese-German University
Slide 04
100% Commitment Fulfillment Status
✔ Trajectory Execution (R2/R3): Streamed /joint_states at 50 Hz to 6 ArticulationBodies with zero sagging and smooth tracking (100% DONE).
✔ Grasping Mechanism (R4): Implemented industrial Attach/Parenting logic in GripperController.cs with instant latching (100% DONE).
✔ Closed-Loop Sequencer (R4): Constructed 7-step autonomous sequencer (task_state_machine.py) with zero human intervention (100% DONE).
✔ 3-Bin Sorting System (R4): Deployed Red (Left), Yellow (Right), and Blue (Rear) bins with dedicated non-singular trajectories (100% DONE).
Milestone 1 High-Value Enhancements
⚙ Kinematic Optimization: Locked wrist strictly downward (q4 = 90.0°) & implemented pure base SCARA sweep, cutting cycle time by 65%.
⚙ Realistic PhysX Deceleration: Replaced artificial freezing with pure friction coasting (StopConveyor()) halting cubes at X ≈ 0.00 m (± 3 mm).
⚙ Continuous Multi-Item Flow: Upgraded Spawner to maintain 2-3 items on conveyor simultaneously with safe 38cm spacing.
⚙ Empirical QA Logging: Integrated automated CSV logger recording 70 consecutive trials with 100% reliability for Milestone 1 defense.

## Slide 5
ARCHITECTURE
System Architecture: Bidirectional Communication Pipeline
UC8 Robotic Sorting Workcell | Milestone 1 Defense | Vietnamese-German University
Slide 05
Layer | Key Responsibility | Topic / Protocol | Rate & Direction
Unity Perception | Detects cube, halts conveyor, converts frame to ROS FLU | /detected_object_pose, /detected_object_type | 10 Hz (Unity -> ROS)
ROS-TCP-Endpoint | Low-latency network bridge brokering serialised ROS messages | TCP Port 10000 Socket Streaming | Real-time (Bidirectional)
State Machine | Closed-loop task logic sequencing 7 execution states | task_state_machine.py orchestrator | Event-driven (ROS Node)
MoveIt Core | Plans collision-free Cartesian paths & joint trajectories | manipulator MoveGroupCommander | MoveIt <-> State Machine
Robot Controller | Maps joint positions to 6 UR10e ArticulationBodies | /joint_states (JointTrajectoryPoint) | 50 Hz (ROS -> Unity)
Gripper Controller | Parenting attach logic; animates fingers and clamps cube | /ur10e/gripper_command, /gripper_status | Event-driven (ROS <-> Unity)
CORE INTERFACE SPECIFICATIONS & STANDARDS
• Coordinate Mapping: X_ROS = Z_Unity, Y_ROS = -X_Unity, Z_ROS = Y_Unity • Planning Group: manipulator | Planning Frame: base_link | End Effector: tool0 • Streaming Topics: /detected_object_pose (Pose), /detected_object_type (String), /joint_states @ 50 Hz, /ur10e/gripper_command (Bool)

## Slide 6
FEEDBACK & ISSUE RESOLUTIONS
Instructor Feedback and Solving Runtime Engineering Challenges
UC8 Robotic Sorting Workcell | Milestone 1 Defense | Vietnamese-German University
Slide 06
Instructor Feedback
Requirement: Visible 2-Finger Claw
• Faculty Feedback: Instructor requested a visible mechanical gripper claw on the robot rather than an abstract suction/contact point.
• Procedural Claw (VisualClaw): Designed flange adapter (1.2cm), navy housing chassis (2.0cm), and dual-color status LED (Cyan/Emerald).
• Industrial Fingers: Aircraft aluminum arms (4.0cm) with high-friction black rubber pads; animated carriage (9.2cm to 6.1cm span).
Runtime Issue 1
Challenge: Missed Cubes in Continuous Flow
• Observed Bug: Over extended runs, cubes occasionally slipped past pick station due to missed trigger collisions.
• Root Cause: OnTriggerEnter is fragile under continuous multi-item flow and physics frame discretization.
• Technical Solution: Replaced trigger collisions with continuous active scanning (FindLeadingCubeOnConveyor()) + safety stop latch at X >= -0.015m (100% reliable).
Runtime Issue 2
Challenge: Conveyor Penetration & Off-Axis Twist
• Observed Bug: Claw slightly penetrated belt during descent; upon grasping, cube twisted off-axis by 13.6°.
• Root Cause: Tool orientation was skewed (0.7854 quaternion), and forced position/rotation snapped cube off-axis.
• Technical Solution: Standardized down_orientation = Quaternion(0.7071, 0.7071, 0, 0), elevated fingertips (+2.3cm clearance), and pure parenting.

## Slide 7
LAYOUT OPTIMIZATION
Workcell Layout: Front Pick Zone and Flanking Bins
UC8 Robotic Sorting Workcell | Milestone 1 Defense | Vietnamese-German University
Slide 07
Component | Selected Setup | Engineering Rationale
Conveyor | 3.6 m, centered directly in front (X = -0.60 m) | Stable transport through robot workspace; ample gliding run
Pick zone | Front center (X = -0.60 m, Y = 0.00 m) | Symmetric approach minimizing arm travel distance & inertial moments
Red and yellow bins | Left (Y = +0.55 m) and right (Y = -0.55 m) | Clear transfer paths eliminating collision hazards with conveyor
Blue bin | Behind robot (X = +0.50 m, Y = 0.00 m) | Separates third sorting target via pure base shoulder pan rotation
Support surface | 4.0 m × 2.0 m heavy industrial table | Rigid mechanical foundation for rails, bins, and robot fixtures
SPATIAL CLEARANCE & SAFETY DIMENSIONS
• Bin Mouth Enlargement: Expanded +35% to 0.38 m × 0.38 m × 0.10 m for 100% free-fall capture rate. • Vertical Safety Envelopes: +16 cm Pre-grasp & Lift altitude completely clears conveyor aluminum rails (Z = +0.10 m) with zero contact.

## Slide 8
KINEMATICS
Downward Wrist Orientation and Transfer Motion
UC8 Robotic Sorting Workcell | Milestone 1 Defense | Vietnamese-German University
Slide 08
Motion Strategy
✔ Downward tool orientation: tool0 remains vertical ([0, 0, -1]) during approach, grasp and release via locked wrist (q4 = 90.0°).
✔ Pre-grasp waypoint: The robot approaches above the target (+16cm) before descending.
✔ Vertical descent: The final approach moves along pure Cartesian Z, avoiding contact with conveyor rails.
✔ Lift before transfer: The cube clears the conveyor (+16cm) before base rotation begins.
✔ Dominant shoulder pan: The transfer uses a large base rotation while other joints remain stable like a SCARA crane.
Joint Values across Poses (Radians)
⚙ Standby pose: [0.2945, -1.4760, -2.1278, -1.1022, 1.5708, 0.5291]
⚙ Red bin (left): [-1.0741, -1.4731, -2.2727, -0.9602, 1.5708, 0.5291]
⚙ Yellow bin (right): [1.7077, -1.4731, -2.2727, -0.9602, 1.5708, 0.5291]
⚙ Blue bin (rear): [-2.7858, -1.3576, -2.3651, -0.9833, 1.5708, 0.5291]
⚙ Kinematic Invariance: Shoulder lift, elbow, and wrist joints stay within 0.15 rad across all bins; only shoulder pan swings widely.

## Slide 9
PHYSICS AND VISUALS
Conveyor Motion and Pick-Zone Stopping
UC8 Robotic Sorting Workcell | Milestone 1 Defense | Vietnamese-German University
Slide 09
Runtime Behaviour & Friction Deceleration
✔ Transport: Objects move at configured conveyor speed (rock-steady 0.30 m/s).
✔ Detection: Pick-zone sensor actively identifies leading SortableObject cube.
✔ Stop: At X >= -0.015 m, conveyor cuts power. Friction halts cube smoothly at X ≈ 0.000 m (± 3 mm).
✔ Zero Teleportation: Strictly eliminates artificial coordinate snapping or kinematic freezing.
✔ Resume: Conveyor restarts automatically after cube handling and release into bin.
Multi-Item Flow & Visual Rig Consistency
⚙ Continuous Multi-Item Flow: Upgraded Spawner maintains 2-3 active cubes on belt simultaneously, providing continuous sorting.
⚙ Anti-Stacking Spacing: Strict 38 cm minimum spacing (IsSpawnAreaClear()) prevents any cube collisions at spawn head.
⚙ Visual consistency: Belt texture scrolling is synchronized 1:1 with physical object motion at 0.30 m/s.
⚙ Mechanical Rig Structure: Ribbed rubber belt, dual aluminum guide rails, dual chrome rollers, and gearmotor unit.
⚙ Optical Sensor LED: Dual-color indicator displays Green when running, switching to Red when cube stops at pick center.

## Slide 10
AUTOMATION PIPELINE
7-Step Closed-Loop Task State Machine Execution
UC8 Robotic Sorting Workcell | Milestone 1 Defense | Vietnamese-German University
Slide 10
Step | State Name | Primary Action | Safety & Validation Guard
1 | STANDBY | Arm hovers above pick station (Z = 0.42 m) | Elbow held elevated; wrist strictly downward
2 | APPROACH | Rapid Cartesian descent to Pre-grasp Pose (+16cm) | Clears conveyor rails in < 0.5s; wait=True feedback
3 | DESCENT | Vertical Cartesian descent to contact (+6.5cm) | Fingertips float 2.3cm above belt (zero sinking)
4 | GRASP | Publish gripper command (True); latch object | Attach logic latches cube; MoveIt updates PlanningScene
5 | LIFT | Linear Cartesian lift back to safe height (+16cm) | 10cm vertical lift clears conveyor rails without snagging
6 | MOVE_TO_BIN | Single shoulder pan rotation to destination bin | Non-singular trajectory avoids table collisions
7 | RELEASE | Publish gripper command (False); release cube | Parenting detached; gravity drops cube into bin
8 | READY / REARM | Arm returns to Standby pose over pick zone | Resumes conveyor & triggers spawner for next cycle

## Slide 11
QUALITY ASSURANCE
Empirical Test Benchmark: 70 Consecutive Trials
UC8 Robotic Sorting Workcell | Milestone 1 Defense | Vietnamese-German University
Slide 11
Performance Metric | Requirement | Empirical Measured Result | Status Evaluation
Total benchmark trials | >= 10 cycles | 70 consecutive cycles logged | Exceeds requirement by 700%
Grasp success rate | >= 90.0% | 100.0% (70 / 70 trials) | Perfect reliability; zero drops
Bin sorting accuracy | >= 90.0% | 100.0% (70 / 70 trials) | 100% correct bin routing
Mean cycle time | < 30.0 s | 11.23 s (Min: 10.8s, Max: 12.1s) | 2.7x faster than threshold
Conveyor transport speed | 0.2 - 0.5 m/s | 0.30 m/s rock-steady velocity | Optimal industrial pace
Coasting stop deviation | <= 20 mm | +- 3 mm repeatable halt | High physical precision

## Slide 12
TECHNICAL DEFENSE
Faculty Committee Engineering Defenses
UC8 Robotic Sorting Workcell | Milestone 1 Defense | Vietnamese-German University
Slide 12
Why are Pre-grasp and Lift poses necessary?
• Industrial workcells divide workspace into Free-space transit and Fine Cartesian approach.
• Pre-grasp (+16cm) establishes a collision-free holding waypoint above the moving conveyor.
• Moving directly on diagonal paths risks collision with conveyor rails or bin edges.
Why avoid fixed sleep delays for motion timing?
• Motion time varies with distance (1.07 rad to Red bin vs 2.78 rad to Blue bin).
• Fixed sleep delays cause premature grasp triggers (dropped objects) or unnecessary idle time.
• MoveIt trajectory execution feedback (wait=True) confirms physical arrival before next step.
How were ragdoll sagging & oscillations eliminated?
• 1. base_link locked with immovable = true in ArticulationBody.
• 2. Gravity disabled (useGravity = false) on arm links; gravity compensation handled by MoveIt dynamics.
• 3. Tuned high PhysX drive stiffness (stiffness = 50000, damping = 1000, forceLimit = 10000).

## Slide 13
WEEK 06 OBJECTIVES
Week 06 Sprint: Fulfilling Requirement R5 & Robustness
UC8 Robotic Sorting Workcell | Milestone 1 Defense | Vietnamese-German University
Slide 13
R5 Conveyor Robustness
• 5-Minute Continuous Operation: Validate that conveyor, spawner, and sensor run non-stop without jamming.
• Variable Velocity Modulation: Support dynamic speed adjustment (0.1 to 0.5 m/s) via ROS parameter service.
• PhysX Friction Stability: Eliminate micro-slip across diverse cube weights (0.1kg - 0.5kg).
Deterministic Spawner
• PRNG Seed Reproducibility: Implement seed parameters for RandomObjectSpawner.cs.
• Guaranteed Test Batches: Allow exact sequence replay (e.g. Red -> Blue -> Yellow) for automated regression.
• Spacing Latch Verification: Guarantee 38cm spacing under all belt acceleration profiles.
Fault Recovery
• Belt Jam Auto-Recovery: Automated reverse-and-clear logic if an unexpected stall occurs.
• Perception Timeout Guard: Fail-safe state machine rollback if object detection frame drops.
• Socket Watchdog: Auto-reconnect handling for ROS-TCP-Endpoint in case of network hiccups.
WEEK 06 DEFINITION OF DONE
• Complete fulfillment of Requirement R5 (Conveyor & Spawner Integration). • The workcell runs hands-free for > 5 minutes with zero cube miss, zero jam, and deterministic regression logging.

## Slide 14
MILESTONE 2 STRATEGIC ROADMAP
Milestone 2 (Week 10): Static Obstacle Avoidance & Perception
UC8 Robotic Sorting Workcell | Milestone 1 Defense | Vietnamese-German University
Slide 14
R5 & R6: Conveyor & Vision
• R5 (Continuous Conveyor): Industrial belt running continuous multi-item queues with zero jam.
• R6 (Computer Vision Pipeline): Camera perception module replacing metadata detection.
• Color Classifier: OpenCV HSV segmentation classifying Red, Blue, and Yellow cubes under varying lighting.
R7: 3D Localization
• Camera-to-Robot Calibration: Hand-eye calibration linking camera pixel coordinates to UR10e base_link.
• Centroid Extraction: Projecting bounding box centroids to 3D Cartesian coordinates.
• Localization Accuracy: Benchmarked measurement error <= 20mm compared to ground truth.
R8: Static Obstacle Avoidance
• Static Wall Barrier: Introducing physical obstacle wall between pick station and sorting bins.
• MoveIt PlanningScene: Real-time obstacle representation in collision matrix.
• Collision-Free Detour: OMPL planner automatically computes curved bypass paths around the wall.
MILESTONE 2 (WEEK 10) ACCEPTANCE CRITERIA: STOP-AND-PICK MODE
• Verification of Requirements R5, R6, R7, and R8 in Stop-and-Pick mode (conveyor stops before grasp). • Arm successfully navigates around static obstacle barrier with zero collision across >= 20 benchmark trials.

## Slide 15
MILESTONE 1 CONCLUSION
Summary of Deliverables & Official Acceptance Sign-Off
UC8 Robotic Sorting Workcell | Milestone 1 Defense | Vietnamese-German University
Slide 15
Requirements Met
✔ R1 (Architecture & Scope): 100% Approved
✔ R2 (UR10e MoveIt Planning): 100% Operational
✔ R3 (ROS-Unity Bridge): 100% Low-Latency Streaming
✔ R4 (Closed-Loop Pick & Place): 100% Autonomous
Empirical Evidence
✔ 70 Consecutive Trials Logged
✔ 100.0% Grasp Success Rate
✔ 100.0% Multi-Bin Placement Rate
✔ 11.23s Mean Cycle Time (2.7x faster)
Deliverables Package
✔ Git Tag Release: m1-verified
✔ Complete trials.csv QA Evidence
✔ Clean run_workcell.sh Launcher
✔ Multi-Camera Demo Visuals
FORMAL MILESTONE 1 ACCEPTANCE REQUEST
• All commitments made for Milestone 1 have been 100% fulfilled and reinforced with faculty feedback solutions. • The UC8 sorting workcell is fully verified and ready for formal Milestone 1 sign-off and progression to Week 06 / Milestone 2.